Foreword
CBL_GC_SOCKET / cob_socket is a general usabke socket library. It can be used for communication between multiple processes (one server, unrestricted number of clients) – on the same or on different machine.
It may be used by COBOL (using the name CBL_GC_SOCKET and alternatively the legacy-name CBL_OC_SOCKET) and by C/C++ and all programming languages that are possible to call these.
As socket-communication is not limitted to a specific system it can be used to communicate between programs written in different programming languages, too.
It may also be used to replace ACUCOBOL-GTs callable system library C$SOCKET in COBOL programs (including, but not limitted to, GnuCOBOL, OpenCOBOL, ACUCOBOL-GT).
Provided functions

1 GENERAL
COBOL always calls the same module. A function code determines which function should be performed. The module must be loaded via COB_PRE_LOAD.

2 CALLING AND EXECUTING
Calling a function under COBOL has the following structure:

CALL "CBL_GC_SOCKET"
        USING function-code [Parameter1 [, Parameter2 [, ...]]]
        GIVING return-value
END-CALL

The function code is a PIC X (2). The number and form of the parameters depends on the respective function.

The return value is a PIC 9 (3) and should always be evaluated to detect possible errors. There are the following general return values, which can be supplied by all functions (except function 99):

Return value	Description
98	General error in a function that cannot be specified. In such a case, calling the last OS / socket error detection function (code 99) may provide further information.
99	Incorrect parameter or wrong number of parameters when calling a function.

It should be noted that for parameters that are filled by calling the function
no constants are to be used !!!

3 STANDARD FUNCTIONS
The following functions are suitable for general socket communication.

Function code	Description
00	Opens a server socket on the specified port. If successful, the server socket handle, which is necessary for later actions, is stored in the second parameter. / Note: Even after these features succeed, clients can connect to the socket and also send data. Functions 01 and 07 only take the accumulated connections out of the wait loop to work with them. / Parameter 1: port number, PIC X(5), IN / Parameter 2: server socket handle, PIC X(4), OUT / Returns: / 0 - success / 1 - port is not available / server is already running / 2 - invalid connection handle / no connection
O P E N
01, 07	Waiting for a connection from a client. This function can only be called with a server socket handle. / If successful, the server socket is closed in function 01 and the connection handle is stored in the first parameter. In function 07, the server socket remains open and the connection handle is stored in the second parameter. / The connection handle is needed for later actions. / Function 01: / Parameter 1: server socket / connection handle, PIC X(4), IN/OUT / Function 07: / Parameter 1: server socket handle, PIC X(4), IN / Parameter 2: connection handle, PIC X(4), OUT / Returns: / 0 - success / 1 - no socket open / 2 - Socket does not "listen“
A C C E P T
02	Connects to a server (socket). If successful, the connection handle is saved in the 3rd parameter. / The connection handle is needed for later actions. / Parameter 1: IP adress, PIC X(15), IN / Parameter 2: port, PIC X(5), IN / Parameter 3: connection handle, PIC X(4), OUT / Returns: / 0 - success / 1 - address / port not available / opposite side not ready / 2 - connection already exists / 3 - invalid connection handle / no connection
C O N N E C T
03	Sends data via a valid connection handle. / Parameter 1: connection handle, PIC X(4), IN / Parameter 2: number of bytes to send, PIC X(5), IN / Parameter 3: data to be send, PIC X(n), IN / Returns: / 0 - success / 2 - fewer bytes were sent than desired / 3 - invalid connection handle / no connection (attention, in this case a "98 - general error" may be returned instead) / 4 - number of bytes exceeds operating system limit
W R I T E
04, 08	Receives data via a valid connection handle. With function 08, a timeout can be specified in milliseconds to only wait for a certain period of time for incoming data. / Timeout with value zero or function 04 waits endlessly. / After receiving, the number of bytes received is stored in parameter 2. / Parameter 1: connection handle, PIC X(4), IN / Parameter 2: number of bytes to send / actually sent, PIC X(5), IN/OUT / Parameter 3: buffer for the received data, PIC X(n), OUT / Only function 08: / Parameter 4: timeout in milliseconds, PIC X(6), IN / Returns: / 0 - success / 1 - an attempt was made to receive more than 64000 bytes / 2 - fewer bytes were read than desired / 3 - invalid connection handle / no connection (attention, in this case a "98 - general error" may be returned instead) / Only function 08: / 4 - timeout expired
R E A D
05	Send data and wait for completion. This function is a combination of functions 03 and 04. / Parameter 1: connection handle, PIC X(4), IN / Parameter 2: number of bytes to send, PIC X(5), IN / Parameter 3: number of bytes to receive / actually received, PIC X(5), IN/OUT / Parameter 4: buffer for the data to be sent / received / Returns: / 0 - success / 1 - there were fewer bytes sent than desired / 2 - data to be sent exceeds the limit of the operating system / 3 - an attempt was made to receive more than 64000 bytes / 4 - fewer bytes were received than desired / 5 - invalid connection handle / no connection
W R I T E – A N D – R E A D
06	Closes a connection or a server socket. / Parameter 1: server socket / connection handle, PIC X(4), IN / Returns: / 0 - success / 1 - invalid connection handle / no connection
C L O S E
09, 10	Waits for an inbound connection of a server socket or incoming data on one of the internally managed existing connections. The newly connected socket connection or the connection that holds data is delivered. / Timeout with value zero or function 09 waits endlessly. / Note: All connections accepted through these functions are stored and managed internally in a pool. The number is theoretically not limited. To ensure that the handles in the pool remain consistent, it is important to explicitly close connection handles that are no longer needed with function 06. This will remove connections from the pool even if the closure fails due to an error. / Parameter 1: server socket, PIC X(4), IN / Parameter 2: connection handle, PIC X(4), OUT / Only function 10: / Parameter 3: timeout in milliseconds, PIC X(6), IN / Returns: / 0 - success / 1 - no (server) socket open / 2 - socket does not "listen" / 3 - server socket is in the set of active connections / 4 - One of the active connections / the server socket is invalid / Only function 10: 5 - timeout expired
N E X T – R E A D
98, 99	Returns the last error of the operating system or the socket layer. Function 98 offers the possibility to provide not only the error code but also a descriptive text of the error. / Hinweis: BFunction 98 does not check if a buffer has been passed because error code 99 is also used by the operating system and therefore cannot be returned by "CBL_GC_SOCKET" in this situation. The error text may contain a line break. If this text is to be output in a log, an "inspect Puffer converting x'0D0A' to spaces" is useful. / Only function 98: / Parameter 1: buffer for textual errors, PIC X(256), OUT / Returns: / last error code, PIC X(3), OUT
S H O W – E R R O R